## Slide 1: Emulators & IOC testing

## Slide 2: Simulating a device
Recsim:
  Easy to set up – just need a few simulation records in the IOC
  Can test records but not the protocol file
  Limited capabilities, has to be done in DB records. Typically just a “value holder”.
Devsim:
  Slightly harder to set up – need to define a device and stream adapter in Lewis
  Can test the full IOC – both db records and protocol file
  Written in Python, so easy to do complex manipulations if required
  Stateful simulations make it easier to simulate complex device behaviours
  Can manipulate the device’s parameters “on the fly” via the back door – useful for testing error conditions

## Slide 3: Recsim (Extract from eurotherm)
### SIMULATION RECORDS ###
record(ai, "$(P)SIM:MAX_OUTPUT")
{
field(SCAN, "Passive")
field(DTYP, "Soft Channel")
}
alias("$(P)SIM:MAX_OUTPUT",
"$(P)SIM:MAX_OUTPUT:SP")
alias("$(P)SIM:MAX_OUTPUT",
"$(P)SIM:MAX_OUTPUT:SP:RBV")
record(bo, "$(P)SIM")
{
field(SCAN, "Passive")
field(DTYP, "Soft Channel")
field(ZNAM, "NO")
field(ONAM, "YES")
field(VAL, "$(RECSIM=0)")
}
record(ai, "$(P)MAX_OUTPUT") {
field(DESC, "Max Output Readback")
field(INP, "@eurotherm2k.proto readIt $(PORT)")
field(SIML, "$(Q)SIM")
field(SIOL, "$(P)SIM:MAX_OUTPUT")
}

## Slide 4: Devsim (Lewis) - components
Stream interface:
  Defines how the device should send and receive data from the IOC
  Should parse & format commands in and out.
Device:
  Holds the values of the device’s internal variables and might define non-stateful interactions between them.
  Should not depend on the format of sent commands
States:
  Used for more complex simulations to define (for example) the progression of a variable over time
  Lewis contains features which can help to give more advanced features, for example linear approach towards a setpoint.

## Slide 5: Devsim (Lewis) – examples
Stream interface
Format data for the device, for example from hex input/output on the serial line to an integer internally
def set_position(self, value):
self._device.set_position(int(value, 16)) def get_position(self):
return “P{:04X}”.format(self._device.get_position())
def get_position(self):
return self.position
def set_position(self, value):
self.position = value
Device
Holds the values and might perform manipulations that don’t depend on the device’s state.

## Slide 6: Devsim (Lewis) – state examples
class StoppingState(State):
def in_state(self, dt):
device = self._context
device.set_speed(approaches.linear(
device.get_speed(), 0, 0.1, dt))
State
Perform stateful manipulations of the data, e.g. approach a setpoint linearly.
def _get_state_handlers(self):
return {‘going': GoingState(),
'stopped': StoppedState(),
'stopping': StoppingState() }
def _get_initial_state(self):
return ‘stopped’
def _get_transition_handlers(self):
return OrderedDict([
((‘stopped', ‘going'), lambda: self.motor_enabled is True),
((‘going', 'stopping'), lambda: self.motor_enabled is False),
(('stopping', 'stopped'), lambda: self.speed == 0),
])

## Slide 7: Connecting LeWiS to the IOC
Start LeWiS with a command like:
  lewis -r 127.0.0.1:10000
  -p stream
  -a C:\Instrument\Apps\EPICS\support\DeviceEmulator\master
  -k lewis_emulators my_device
  -- --bind-address localhost --port 57677
Start the IOC in Devsim mode, ensure the port is the same as above!
You should see the following in the LeWiS log:
  lewis.FermichopperStreamInterface.StreamServer: Listening on 127.0.0.1:57677
  lewis.FermichopperStreamInterface.StreamHandler: Client connected from 127.0.0.1:54313
If you can’t get it to work, see https://github.com/ISISComputingGroup/ibex_developers_manual/wiki/Emulating-Devices#troubleshooting

## Slide 8: IOC testing framework
Runs tests against the IOC in both Recsim and Devsim modes
Fairly new to the project, so if you find something missing, add it!
Runs on Jenkins
Verify that IOC behaviour is unchanged when making changes to it

## Slide 9: IOC testing framework - setup
st.cmd should be modified to use the EMULATOR_PORT macro in devsim mode. For newer IOCs this command will already exist.
  ## For unit testing:
  $(IFDEVSIM) drvAsynIPPortConfigure(
  "$(DEVICE)", "localhost:$(EMULATOR_PORT=)")
To add a another suite of tests:
  Create a Python file with the same name as the Lewis device (for example: linkam_t95). This should be lowercase.
  Create a class in it with the same name as the file but with the first letter capitialised and "Tests" appended (for example: Linkam_t95Tests).
  Fill the class with tests.
  Add your new tests to run_all_tests.bat, this is the easiest way to run your new tests.

## Slide 10: IOC testing framework - logs
The IOC test framework writes logs to C:\Instrument\Var\logs\IOCTestFramework
You can force extra debug output by:
  Adding @has_log at the top of the class
  Using self.log.debug(“message”)
  log.info, log.warning and log.error are also available

## Slide 11: IOC test framework – structure of a test
class MydeviceTests(unittest.TestCase):
# Runs before every test def setUp(self):
# Grab a reference to the ioc and lewis self._lewis, self._ioc = get_running_lewis_and_ioc(“mydevice")
# Setup channel access with a default timeout of 20 seconds self.ca = ChannelAccess(20)
# Wait for a PV to be available – the IOC may take some time to start self.ca.wait_for(“IOCNAME_01:DISABLE", timeout=30) def test_WHEN_ioc_is_started_THEN_ioc_is_not_disabled(self):
# Assert that a PV has a particular value (prefix prepended automatically) self.ca.assert_that_pv_is(“IOCNAME_01:DISABLE", "COMMS ENABLED")
Try to use GIVEN_WHEN_THEN test naming wherever appropriate

## Slide 12: IOC testing framework – setting values
Set via channel access:
Set via Lewis backdoor:
  This is an “on-the-fly” modification of the device’s internal parameters
  Use this to set values that you wouldn’t be able to set via the IOC
  Can be useful to check the IOC’s response to error conditions.
self.ca.set_pv_value(“MYIOC_01:PRESSURE:SP", value)
self._lewis.backdoor_set_on_device("pressure", value)

## Slide 13: IOC test framework - assertions
A number of assert statements are available* in the test framework:
  assert_that_pv_is
    Checks that a PV has a particular value (exact).
  assert_that_pv_is_number
    Checks that a PV is a number, within a specified tolerance.
  assert_that_pv_is_integer_between
    Checks that a PV is an integer between two specified bounds.
  assert_pv_alarm_is
    Checks that a PV has a particular alarm state.
  assert_setting_setpoint_sets_readback
    Checks that a PV is a particular value after the relevant setpoint is changed.
If you find yourself needing other assert functions, please add them!
(*) some of these functions might still be on branches at this stage

## Slide 14: IOC test framework – skip tests in RECSIM
Recsim is not as advanced as devsim – for any reasonably complex emulator, the emulator will have some functionality which recsim doesn’t
To test these bits of functionality, add the following annotation to tests which should only run in DEVSIM mode:
Any test which includes a lewis backdoor command MUST have this annotation, otherwise it will error because it can’t find lewis in RECSIM mode
@skipIf(IOCRegister.uses_rec_sim, "In rec sim this test fails") def test_GIVEN_condition_WHEN_thing_is_done_THEN_thing_happens(self):
# Some functionality which doesn’t exist in recsim goes here

## Slide 15: IOC test framework – avoid test-ordering races
When run by the IOC test framework, the IOC + emulator state persists between tests
For simple tests/emulators this is not typically an issue, but for complex emulators this can cause tests to pass when run on their own but fail when run as part of a suite, or fail intermittently. This can be very hard to debug!
Solution is to ensure a consistent startup state in the setUp method of the tests.
This will run before each test, and it should “reset” all relevant properties of the device so that each test always starts from a consistent starting state
Doing lots in the setup method will make the tests run a bit slower – this is preferable to having inconsistently passing tests!

## Slide 16: IOC test framework – parametrized tests
You can create tests which check a few values
e.g. boundaries, negative numbers, zero, floats and integers (if applicable to the device)
Testing different types of values can quickly catch simple errors in the IOC’s records or protocol file, for example accidentally having a %i (integer) instead of %d (double) format converter.
def test_WHEN_speed_setpoint_is_set_THEN_readback_updates(self): for speed in [0, 0.65, 600]:
self.ca.set_pv_value(“MYIOC_01:SPEED:SP", speed) self.ca.assert_that_pv_is(“MYIOC_01:SPEED:SP:RBV", speed)

## Slide 17: IOC test framework – rounding errors
For a non-trivial IOC you might get rounding errors
e.g. setpoint = 2.5, readback = 2.4997
This assertion lets you define a tolerance range, within which the assertion will pass.
def test_WHEN_speed_setpoint_is_set_THEN_readback_updates(self): self.ca.set_pv_value(“MYIOC_01:SPEED:SP", speed) self.ca.assert_that_pv_is_number(“MYIOC_01:SPEED:SP:RBV", speed, tolerance=0.01)

## Slide 18: IOC test framework – test PINI records
If you have a record which is only processed at initialization (i.e. PINI=Yes, SCAN=Passive), you can test this by forcing it to process:
def test_ioc_name(self):
self._lewis.backdoor_set_on_device(“name", “new_name”)
# Force record to process and therefore get new value from emulator: self.ca.set_pv_value(“MYIOC_01:NAME.PROC", 1) self.ca.assert_that_pv_is(“MYIOC_01:NAME", “new_name")